HTML:

https://www.inetdaemon.com/tutorials/internet/tcp/3-way_handshake.shtml

TCP: Transmission Control Protocol.

Connection oriented. It’s slower than UDP.

Reliable protocol, will set up a connection and will verify that all data transmitted is controlled, ordered, received in the correct order and intact.

The error correction, ordering and verification mechanisms require overhead in data packets and increase the amount of bandwidth needed.

Http, https, ftp,ssh, telnet, smtp, pop3, imap, are riding over TCP, and all of them are using 3WH.

Uses three-way handshake, TCP-handshake, three messages handshake or SYN-SYN-ACK, method used by tcp to set up a tcp/ip connection over an internet protocol based network. Are the messages transmitted by tcp to negotiate and start a connection between two computers.

SYNchronize
ACKnowledgement

1 Host A sends a TCP SYN packet to host B → Host B receive A’s SYN
2 Host B sends SYN-ACK → Host A receives B’s SYN-ACK
3 Host A sends ACK → Host B receives A’s ACK
* TCP Socket connection is ESTABLISHED

SYN and ACK messages are indicated a either the SYN bit or the ACK bit inside the TCP Header.
SYN-ACK messages are both syn and ack turned on (set to 1)

When the communication is over another 3-way communication is performed to tear down the tcp socket connection.

TCP Header: The tcp segment (packet is not accurate) have a segment header and a data section.
Header is the first 24 bytes of the segment and contains the parameters and state of an end-to-end tcp socket, so the bit for ack, syn and a lot more of stuff.

Tcp segments are encapsulated (inserted) in the payload of the IP packet, which immediately follows the IP header during the transmission. TCP doesn’t care about the routing, IP is doing that, tcp only tracks which end to end sockets are open.

TCP Sockets: Endpoint instance define by IP and virtual port. Virtual Ports, 0 - 65534

A tcp connection is defined by 2 endpoints.

It is the socket pair (the 4-tuple consisting of the client IP address, client port number, server IP address, and server port number) that specifies the two endpoints that uniquely identifies each TCP connection in an internet. (TCP-IP Illustrated Volume 1, W. Richard Stevens)